## Slide 1: MANE 3351

## Slide 2: Lecture 5

## Slide 3: Classroom Management
Agenda
Arduinos
Reminder: Lab One - due 9/17 before 9:30 AM
There will be a short laboratory session following the lecture

## Slide 4: Resources

## Slide 5: Handouts
Lecture 5 Slides
Lecture 5 Marked Slides

## Slide 6: Assignments
Lab 2 (assigned 9/17/2025, due 9/24/2024 (before 9:30 AM))

## Slide 7: Arduino Uno
Arduino Uno
Source: Arduino Uno Website

## Slide 8
Arduino I/O
Source: Arduino Website

## Slide 9
Input/Output
Voltages - 5V pin and 9V pin are present on the board as well as ground pins (0v)
Digital Pins - multiple digital pins are provided on an Arduino board that can be used for general purpose input and output via the pinMode(), digitalRead(), and digitalWrite() commands
Analog Pins- the analog input pins suport 10-bit analog-to-digital conversion using the analogRead() function
Other Pins - A reference voltage and reset functionality are also available

## Slide 10
Arduino Mega
There are multiple versions of Arduino boards.
The Arduino Mega is often combined with a RAMPS shield to construct homemade Reprap 3D-printers
Arduino Mega and Ramp
Source: all3dp

## Slide 11
RAMPS Shield
Circuit board that plugs into Arduino Mega for build 3D printers
Typically includes drivers for stepper motors shown below
Schematic for 3D printer is also provided below
Both images taken from All3DP website
RAMPS

## Slide 12
3D printer schematic

## Slide 13: Programming Arduino
Written in the Arduino Integrated Development Environment
Arduino programming language is based on a very simple hardware programming language called processing, which is similar to the C language
Programs for Arduinos are called sketches
Sketches must be uploaded to Arduino (via USB cable)
Arduino IDE installed on Raspberry Pi
Source: Programming Arduinos

## Slide 14
Example 1: Blinking an LED
First example is to an LED (same as with the Raspberry Pi)
Arduino LED Circuit

## Slide 15
Example 1: Sketch
Arduino LED Code
Note: there is an error in the sketch. Change digitalRead to digitalWrite

## Slide 16
Code for Blinking an LED
int LED = 13; // the digital pin to which the LED is connected void setup () { pinMode (LED,OUTPUT); //Declaring pin 13 as output ping } void loop () //The loop function runs again and again { digitalWrite (LED,HIGH); //Turn ON the LED delay (1000); //wait for 1 second digitalWrite(LED,LOw); //Turn OFF the LED delay(1000); //wait for one second }

## Slide 17: Warning
Arduinos store the last program in EEPROM and will start running that program as soon as the power is provided
Cautious Approach:
  Do not connect circuit board to Arduino until after the Sketch is loaded
  Afterwards, connect hardware

## Slide 18: Arduino Demonstration 1

## Slide 19: DHT22 Sensor
dht2sensor
Source:

## Slide 20: Technical Details of DHT11 Sensor
dht22 details
Source:

## Slide 21: Arduino Circuit
arduino
Source:

## Slide 22: Arduino Sketch
part 1
Source: Example Code

## Slide 23: Arduino Sketch, continued
part 2
Source: Example Code

## Slide 24: DHT Library
dht Sensor Library
Source:

## Slide 25: DHTest Code
// Example testing sketch for various DHT humidity/temperature sensors // Written by ladyada, public domain // REQUIRES the following Arduino libraries: // - DHT Sensor Library: https://github.com/adafruit/DHT-sensor-library // - Adafruit Unified Sensor Lib: https://github.com/adafruit/Adafruit_Sensor #include "DHT.h" #define DHTPIN 2 // Digital pin connected to the DHT sensor // Feather HUZZAH ESP8266 note: use pins 3, 4, 5, 12, 13 or 14 -- // Pin 15 can work but DHT must be disconnected during program upload. // Uncomment whatever type you're using! //#define DHTTYPE DHT11 // DHT 11 #define DHTTYPE DHT22 // DHT 22 (AM2302), AM2321 //#define DHTTYPE DHT21 // DHT 21 (AM2301) // Connect pin 1 (on the left) of the sensor to +5V // NOTE: If using a board with 3.3V logic like an Arduino Due connect pin 1 // to 3.3V instead of 5V! // Connect pin 2 of the sensor to whatever your DHTPIN is // Connect pin 3 (on the right) of the sensor to GROUND (if your sensor has 3 pins) // Connect pin 4 (on the right) of the sensor to GROUND and leave the pin 3 EMPTY (if your sensor has 4 pins) // Connect a 10K resistor from pin 2 (data) to pin 1 (power) of the sensor // Initialize DHT sensor. // Note that older versions of this library took an optional third parameter to // tweak the timings for faster processors. This parameter is no longer needed // as the current DHT reading algorithm adjusts itself to work on faster procs. DHT dht(DHTPIN, DHTTYPE); void setup() { Serial.begin(9600); Serial.println(F("DHTxx test!")); dht.begin(); } void loop() { // Wait a few seconds between measurements. delay(2000); // Reading temperature or humidity takes about 250 milliseconds! // Sensor readings may also be up to 2 seconds 'old' (its a very slow sensor) float h = dht.readHumidity(); // Read temperature as Celsius (the default) float t = dht.readTemperature(); // Read temperature as Fahrenheit (isFahrenheit = true) float f = dht.readTemperature(true); // Check if any reads failed and exit early (to try again). if (isnan(h) || isnan(t) || isnan(f)) { Serial.println(F("Failed to read from DHT sensor!")); return; } // Compute heat index in Fahrenheit (the default) float hif = dht.computeHeatIndex(f, h); // Compute heat index in Celsius (isFahreheit = false) float hic = dht.computeHeatIndex(t, h, false); Serial.print(F("Humidity: ")); Serial.print(h); Serial.print(F("% Temperature: ")); Serial.print(t); Serial.print(F("°C ")); Serial.print(f); Serial.print(F("°F Heat index: ")); Serial.print(hic); Serial.print(F("°C ")); Serial.print(hif); Serial.println(F("°F")); }

## Slide 26: Demonstration 2 - Temperature/Humidity Sensor